## Slide 1: Hand Sign Gesture Recognition
Iker Vazquez Lopez

## Slide 2
Preprocessing
Extraction
Feature definition and extraction
Laplace filter
Training and classification
ANN
Normalization (depth and size)
Image capture
Ideal world definition
Fourier transform
Gabor filter
…
RDF
…

## Slide 3: Image capture

## Slide 4: Image capture
We are going to use the depth information of the scene to recognize the sign gestures.
  A selection of the capturing sensor is required.
  At this moment we are not going to use any other image source (color, infrared…).
For this thesis an ideal world is going to be defined to capture the images.
  This ensures low environment variance.

## Slide 5: Image capture – Depth sensor types
Time of Flight (ToF)
Low resolution.
High frame rate.
Xbox Kinect
1080px resolution.
Acceptable frame rate.
Different sensor types.
SDK for body tracking.
Stereoscopic camera
Different resolutions.
Different frame rates.
Low depth precision.
Can be built with two normal cameras.

## Slide 6: Image capture – Sensor selection
It is very cheap for the offering resolution and precision.
Depth sensor, color camera and infrared sensor.
30fps enough to track (30>24).
SDK for tracking.
Many people has used it.
  A lot of papers and forums.
Does not work well with bright lighting: use a special environment.
Small optimal range: use a special environment.
Does not capture well the depth map depending on the type of surface.
Kinect

## Slide 7: Image capture – Ideal world definition
White wall for background (no reflective materials).
Subject sitting or standing up? (Select one).
Subject position:
  2m from the Kinect.
  “Center” of the Kinect field of view.

## Slide 8: Preprocessing

## Slide 9: Preprocessing
We are going to focus only on the hands.
  Crop the hands from the original image.
For sign comparing we need to normalize them.
  Size normalization.
  Depth normalization

## Slide 10: Preprocessing – Hand extraction
Kinect camera provides the body information of the user.
  We know where are the hands in the scene → We can crop the image around that part of the scene.
The cropped image contains depth data from the background which it is necessary to discard to keep only the hand.
  Thresholding from the hand joint keeps only the hand depth data.

## Slide 11: Preprocessing – Normalization
People has different hand sizes → the images are different.
Due to the perspective projection of the camera, objects in the back seem smaller than the objects in the front.
  In this case the values of the image are different too, objects in the back have higher depth values (distance).
We can use the body information to scale the hand for normalization.
Compute the average depth value of the hand and translate to a “ideal” location in the 3D space to normalize the depth.

## Slide 12: Feature definition and extraction